## Slide 1
AI-Based Driver Safety and Assistance System(ADAS)
Presented by:
Mohamed Mostafa El-Basyouni (Team Leader)
Michael Magdy Amin Sidhom
Ali Ibrahim Ahmed Othman
Karim Mustafa Ali Ibrahim
Mohamed Osama Bahnasy Abdel Halim
ABSTRACT
RESULTS
SentryEye is an on-device AI driver safety system that detects eye closure and yawning in real time. Using YOLO26n, PERCLOS, and micro-event analysis, the system interprets fatigue levels and delivers visual and audio alerts directly in the browser without uploading video.
To develop a real-time, camera-based driver drowsiness detection system that combines reliable computer vision with temporal fatigue analysis and privacy-preserving browser deployment.
SentryEye demonstrates that real-time driver drowsiness detection can be deployed directly in the browser without transmitting video to a remote server. Visual detection, PERCLOS, and real-time alerts provide a practical foundation for privacy-preserving driver safety.
Under Supervision of:
[ DR. Kamel Elhadad ]
https://sharp-gaze-platform.lovable.app
https://dashboard-grad-project.vercel.app
IMAGES · 68,292 ANNOTATED INSTANCES
39,627
TRAIN
5,438
VAL
5,589
TEST
3 CLASSES
closed_eye
open_eye
yawning
Augmentation: HSV jitter, rotation, shear, translation, random erasing (moderate + worst-case tiers).
Mosaic / mixup / copy-paste deliberately disabled.
50,654
86.75%
mAP@50
mAP@50
86.75%
90.23%
89.23%
88.38%
97.2 FPS
Recall
Inference Speed
Precision
F1-Score
Camera / Video Input
Frame Processing
YOLO26n Inference
PERCLOS + Micro-events
Debounced Alert State
HUD + audio alert + safety report follow the debounced state machine. Every node, arrow, and label is editable.
Aim of the work
SentryEye
AI-BASED DRIVER SAFETY AND ASSISTANCE SYSTEM
REAL-TIME DROWSINESS DETECTION.
SMARTER ALERTS. SAFER ROADS.
A fully on-device, browser-native AI system that detects driver fatigue through eye closure, yawning, PERCLOS, and micro-event analysis.
QR CODE
Conclusion
  SYSTEM OVERVIEW
  METHODOLOGY
1. Dataset Construction → Data Cleaning
& Label Collection
Dataset Construction · Data Cleaning & Label Collection · Model Training · Cross-Model Evaluation
2. Production Pipeline → Browser Deployment
Model Selection · ONNX Export · WebGPU / WASM Deployment · Temporal Fatigue Analysis · Real-Time Alerting
Production model: YOLO26n at 480px and 960px, exported to ONNX and executed in-browser through WebGPU / WASM.
Only the replaceable icons are decorative; the shapes, arrows, and text all remain editable.
DATASET
THE PROBLEM
OUR SOLUTION
AI MODELS
Future Work
Driver fatigue is a leading cause of road traffic collisions. Prolonged eye closure and yawning are visible warning signs — but existing detection datasets are too fragmented and inconsistently annotated to build a reliable detector directly.
SentryEye detects three visual states per frame — closed eye, open eye, yawning — then aggregates them into a rolling PERCLOS score and a debounced SAFE / WARNING / CRITICAL alert, so a single misdetection never triggers a false alarm.
4 architecture families compared under one protocol:
YOLO26 (n / s) · YOLOv11 (n / m) · RF-DETR (Nano / Small) · Faster R-CNN (custom)
21 trained configurations
950 epochs · 277.6 GPU-hours (RTX 2000 Ada)
Production model: YOLO26n – 480px & 960px + ONNX + WebGPU / WASM
Learned temporal modeling (RNN / LSTM) for blink & yawn duration
Multi-task learning — facial landmarks + gaze
Multi-camera support
Context-aware driver personalization
USED TOOLS
KEY FEATURES
Offline-capable — works fully in-browser without needing constant internet connection
Lightweight, on-device deployment — YOLO11n model compressed below 10MB, runs via WebGPU with no server dependency
✅
✅
✅
Our Platform
Offline models
Save a detection model to device once. Live and video detection then start instantly and keep working with no internet connection.
The Privacy
Driver Report
Manger report
The driver will only be able to view his reports status so that he can manage his status to avoid getting fired
Managers can view all drivers' aggregated metrics and multi-month performance histories—without live camera feeds—ensuring privacy and informed decision-making